## Slide 1
Safety and Hazard Analysis (CHE1007) REVIEW-3
[2] Safety and security risk assessment analysis for the solar panel
Team Members:

## Slide 2
LITERATURE REVIEW

## Slide 3
[1] Upholding Safety in Future Energy Systems: The Need for Systemic Risk Assessment
This paper showcases that energy systems are becoming more complex, and it shows how the already existing transition to renewable energy sources has resulted in the emergence of new types of hazards. It demonstrates that the energy sector heavily relies on analytic risk assessment approaches, and that systematic methods provide valuable additional insights. A comparison of the hazard and operability study (HAZOP, analytic) with the system-theoretic process analysis (STPA) in the Dutch gas sector demonstrates this. It emphasises the importance of researching the organisation of protection in energy transitions. The researchers conclude that proper risk management for future energy systems requires both a quantitative and qualitative approach.

## Slide 4
[2] A framework for conceptualizing and assessing the resilience of essential services produced by socio-technical systems
Complex adaptive socio-technical processes generate essential resources like electricity. Continuous structural shifts, such as urbanisation and the rise in the frequency of severe weather, necessitate the resilience of critical services. The paper emphasises the importance of having a dependable and resilient technological infrastructure. The researchers propose a conceptual framework based on a complex adaptive systems perspective that identifies four key domains where investment is needed to strengthen critical services resilience. This structure takes into account both the technological and social aspects of the socio-technical frameworks that provide essential services, as well as specific and broad resilience concerns.

## Slide 5
[3] Adapting the theory of resilience to energy systems
Resilience has gained in importance among the sector of analytic thinking in recent years and has additionally become more and more vital within the thought for energy systems. However, there's no uniform understanding within the literature and therefore the applications dissent.
One reason for this is often that their square measure styles of resilience: engineering resilience, wherever systems square measure placed close to a stable purpose and invariably come back to that when a pause, and ecological resilience, where it's assumed that the system into consideration doesn't rest in associate degree equilibrium however is unendingly in motion. additionally, this kind of resilience assumes many basins of attraction between that associate degree unsustainable system switches, whereas a property system remains in one basin.

## Slide 6
[4] Principles and criteria for assessing urban energy resilience
The framework and criteria introduced during this may be used as a vital preliminary step for development of tools for assessing urban energy resilience. Assessment tools are helpful for informing higher cognitive process by native authorities. Such tools may be used for 3 main purposes: to capture the complexness and effectively change the route to resiliency; to benchmark and live resilience and track action of goals. A point of trade-off between the standards is inevitable and this could be adequately informed. it's hoped that the results of this preliminary work offer helpful steering to increase the scope of the study on assessment of urban energy resilience. Future analysis can have a special concentrate on providing a rather complete understanding of co-benefits and trade-offs between the standards introduced during this study.

## Slide 7
[5] Project risk analysis of solar energy project delays in India
The current strong reliance of the humanity on fossil fuels is seen as a contributing factor to climate change and increasing challenges in meeting renewable energy goals. The use of renewable energy has been proposed as a potential solution to the aforementioned problems. The primary cause of the deficiencies is a lack of risk-mitigation techniques. The effective mitigation of project-related hazards is a critical factor in completing projects on schedule, and it is well within reach.
[6] An integrated management approach of the project and project risk
Rodney proposes modelling, simulating, and evaluating project risks in terms of efficiency, delay, and expense, with the goal of reproducing the project's behaviour, evaluating its results, and anticipating its likely drifts while valuing the following requirements relevant to the entire risk management method.

## Slide 8
[7] Health and safety impacts of solar Photovoltaics
The motive of this paper is to work on public health and safety for utility-scale solar Panels.
The problem was divided in Toxicity, Electromagnetic Fields, Electric Shock and Arc Flash, Fire. In all of this part the problems were shown in very less amount, the negative health and safety impacts of utility-scale PV development were shown to be non-existing , the public health and safety benefits of these facilities are significant and much better than any other resource
[8] The application study in solar energy technology for highway service area:A case study of West Lushan highway low-carbon service area in China
This paper shows the subject of highway and solar energy in a sun based innovation application for highways. This paper has done an investigation on West Lushan parkway lowcarbon administration zone in Jiangxi area of China. The paper demonstrates a decrease of cost on power by the utilization of solar energy. This paper considers solar based traffic signals, sun oriented streetlights, etc. The region powers the utilization of sustainable energy for a low carbon impression on the climate as well as to improve the productivity and efficiency.

## Slide 9
[9] Design of ”Risk and Resilience” Focused Courses for Undergraduate Engineering Education Towards a Hazard-Resilient Built Environment
Since India is growing in the department of infrastructure and hence the intensity and frequency of the hazards like natural non biodegradable are increasing it’s important to report the problem that being faced by environmental so this paper worked on rational object and content of following challenges
The following paper work on following 3 challenges
Information about RISK AND RESILIENCY
Optimization and reliability
Sensing and data analytics for infrastructure systems

## Slide 10
[10]Towards climate resilient urban energy systems
This paper gives an understanding into the advancement that can be accomplished in the energy field to the rising environmental issues and centres around environmental flexibility of metropolitan energy frameworks. The paper defines climate resilience as "an upcoming concept that is used to represent the durability and stable performance of energy systems against extreme climate events". This paper studies and shows a significant disadvantage in the environmental change variation strategies. It also presents the limitations which may occur while connecting the effects of environmental change to different models that attempt to improve it. It provides an insight to the complexity of resilience within the energy system.

## Slide 11
RISK ANALYSIS

## Slide 12
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Working at roof tops | Falling from roof top | Trauma, Broken Bones, Death. | Install scaffolding around roof top with stair access, guard rails. use safety nets; or provide each employee with a body harness that is anchored to the rooftop to arrest a potential fall. | Install ground mounted solar systems avoiding the need to work in an area of high elevation. | High | 
Working with ladders | Falling from ladders. Electrocution | Trauma, Broken Bones, Death. | Place the ladder on dry, level ground removed from walkways and doorways, and at least 10 feet from power lines and secure it to the ground or rooftop. Use a fiberglass ladder with non-conductive side rails near power sources. | Install ground mounted solar systems avoiding the need to work in an area of high elevation. | High | 

## Slide 13
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Lifting and handling solar panels | Can cause strains, sprains, muscle pulls and back injuries | Paralysation, Death. | Transport solar panels onto and around the work site using mobile carts or forklift. Never climb ladders while carrying solar panels. To get solar panels onto rooftops, use properly inspected cranes, hoists or ladder-based winch systems. | Install ground mounted solar systems avoiding the need to work in an area of high elevation. Lift each solar panel with at least two people while applying safe lifting techniques. | High | 
Working with Solar electric systems. | Short circuit, Electric Shocks, electrocution Arc flash, burns | Paralysation, Death. | PPE: Wear arc rated neck to wrist to ankle clothing with a minimum ATPV of 4calm2. Wear protective glasses and gloves and rubber shoes | Cover the solar array with an opaque sheet to “turn off” the sun’s light. Use a meter or circuit test device to ensure that all circuits are de-energized before working on them. Technicians should br properly trained. | High | 

## Slide 14
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Working outdoors. | Exposure to the sun | Exhaustion, fatigue, heat stress . Sun burn, skin cancer | PPE: Slip on clothing, slop on SPF 30+ sunscreen, slap on a hat, slide on sunglasses. Drink plenty of water | Reorganising work schedules where possible so that outdoor tasks are done before 10 am and after 3 pm . Rotating tasks that involve direct sun exposure Increasing amount of shade available – use gazebos | High | 
Working in ceiling spaces | Exposure to poor air quality such as fiberglass, coal dust, lead dust and other harmful substances Exposure to loose- fill asbestos | Respiratory diseases, Cancer, Mesothelioma, asbestosis | PPE: Wearing appropriate, well maintained and correctly-fitted personal protective equipment when working in dusty ceiling spaces, including: a respirator a head covering and goggles, to avoid eye irritation long-sleeved, loose-fitting clothing and gloves | Do not proceed with job until asbestos-containing material removed by licence contractors . Install ground mounted solar systems avoiding the need to work in a ceiling space | Medium | 

## Slide 15
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Earthquake. | Damage of installation | Death, Serious Injury, Massive Financial losses | Use tempered glass to minimise damage to solar panels. The plastic ethylene-vinyl acetate (EVA) commonly provides the cell encapsulation which maximizes its strength. | Don’t construct solar plants in areas of great seismic activity. Insure against any damage from natural calamities. | Low | 
Lightning strike | Direct strikes would destroy/melt panels. Indirect strikes would induce high voltages into the system breaking down conductors, PV panels and producing dangerous sparking that could ignite combustible material. | Death, Serious Injury, Massive Financial losses. | Install air terminals which are interconnected and tied into a grounding ring electrode system for ground-mounted panels where the lightning current will safely dissipate into the earth. Critical to an effective lightning protection system are surge protection devices (SPDs) to suppress lightning induced high voltages to ground and avoid damage to the PV system. | Insure against any damage from natural calamities. Don’t install solar panels in areas of high lightning flash intensity. | Low | 

## Slide 16
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Heavy Winds | Damage of installation | Death, Serious Injury, Massive Financial losses. | Install Wind deflectors, stow or return to flat position quickly. | Insure against any damage from natural calamities. Wind tunnel testing so that it is resistant to high speeds. | Medium | 
Fire | Flammable parts of the solar panel, thin layers of polymer encapsulates surrounding the PV cells will catch fire. | Death, Serious Injury, Massive Financial losses | Non-combustible materials between the panels and the roof will help to create a slight buffer, similarly coupling connections need to be covered securely, to keep the fire from escalating quickly | Insure against any damage from natural calamities. install a shut-off switch to disconnect the solar panels from the electrical system | Medium | 

## Slide 17
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Floods | Damage of installation. High chance of power outage and short circuit, electrocution, burns. | Death, Serious Injury, Massive Financial losses. | Backsheets are made of PET (polyester) due to its thermal and moisture barrier properties. good quality wires and cables also have good resistance to water absorption. Turn of the mains supply, | Sensitive components like inverters or data collection devices mounted with high ground clearance. System should not be switched back until it has been checked by a clean energy council accredited installer or licensed electrician. | Medium | 
Sand storm | Sand particles and dirt accumulate on the solar panels. | Efficiency of solar panels decreases and power output drops | Use automated cleaning system with brush to remove sand. This will improve efficiency. | Insure against any damage from natural calamities. | Low | 

## Slide 18
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Volcano | Clouds of ash and smoke cover the sky blocking sunlight to solar panels and reducing solar PV power output | Death, Serious Injury, Massive Financial losses. Volcanic ash is corrosive and can also damage solar panels and reduce their efficiency. | Use automated cleaning system with brush and cleaning agent to remove volcanic ash which is toxic and jagged. This will improve efficiency. | Insure against any damage from natural calamities. Don’t install panels in volcano prone regions | Very Low | 
Terrorism | Damage of installation, Delay or stop of completion, loss of revenue or project | Death, Serious Injury, Massive Financial losses Loss of credibility | Use of stringent security protection measures, political guarantee. Fences, biometric authentication, metal detectors, in house SWAT team. | Insure against any damage. Restrict access to "high-value" components like inverters. Create physical boundaries to the solar modules. | Low | 

## Slide 19
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Corrosion | Degradation, as rust can affect the critical electronic connections within the panels | Reduce the efficiency and the amount of electricity a solar panel can reduce resulting in Massive Financial losses. | PV panels are encapsulated from air and moisture between two layers of plastic. The plastic ethylene-vinyl acetate (EVA) commonly provides the cell encapsulation | Install good quality solar panels and replace them after 25 years as corrosion due to environmental conditions is inevitable. | High | 
Lead contained in PV cells | the lead in operating PV panels can release to the environment during their service lifetime. | Lead is highly toxic and attacks the brain and central nervous system to cause coma, convulsions and even death. | its internal components, including lead, must be sealed from any moisture. | amount of lead in the panels should be below the RoHS thresholds. (less than 0.10% lead) Discard solar panels after 25 years as there is a higher chance of leeching of lead. | Very Low | 

## Slide 20
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Unacceptable environment al impacts | Encroaching on Protected territory, endangered species, etc | Loss of habitat and life of endangered species. Court case, massive fines | Full Environmental and Social Impact Assessment should be performed to prevent any unfortunate incidents. | Stringent environmental procedures to be followed at construction and operations in accordance to existing laws. | Medium | 
Theft | loss of highly expensive systems like solar modules, inverters, etc. | Massive Financial losses Loss of credibility | Proactive system monitoring will help identify theft quickly. | Design and build elevated solar arrays that would be at least 8 feet above rooftop. Physically attach components with locking bolts. | Medium | 

## Slide 21
Hazard | Consequence | Top Event | Safeguard | Recommendation | Risk Factor | 
Cyber Attack | Compromise all the software systems leading to delay of service, shutdown of plant. | Massive Financial losses Loss of credibility | Install IPS sytems, firewalls, antivirus, etc. | Insure against cyber attacks. Conduct a thorough cyber security audit. | High | 

## Slide 22
RISK MATRIX

## Slide 23
RISK MATRIX
1 | 2 | 3 | 4 | 5
LOW | LOW | LOW | MEDIUM | MEDIUM
1 | 2 | 3 | 4 | 5
LOW | MEDIUM | MEDIUM | HIGH | HIGH
2 | 4 | 6 | 8 | 10
LOW | MEDIUM | HIGH | HIGH | EXTREME
3 | 6 | 9 | 12 | 15
MEDIUM | HIGH | HIGH | HIGH | EXTREME
4 | 8 | 12 | 16 | 20
MEDIUM | HIGH | EXTREME | EXTREME | EXTREME
5 | 10 | 15 | 20 | 25
Likelihood
Severity

## Slide 24
RISK DESCRIPTION | RISK SEVERITY | RISK LIKELIHOOD | IMPACT
Working at roof tops | High (4) | Likely(4) | EXTREME
Working with ladders | High (4) | Likely(4) | EXTREME
Lifting and handling solar panels | High (4) | Likely(4) | EXTREME
Working with Solar electric systems. | High (4) | Likely(4) | EXTREME

## Slide 25
RISK DESCRIPTION | RISK SEVERITY | RISK LIKELIHOOD | IMPACT
Working outdoors. | High (4) | Likely (4) | EXTREME
Working in ceiling spaces | High (4) | Likely (4) | EXTREME
Earthquake | Catastrophic (5) | Unikely (2) | HIGH
Lightning strike | Catastrophic (5) | Unlikely (2) | HIGH

## Slide 26
RISK DESCRIPTION | RISK SEVERITY | RISK LIKELIHOOD | IMPACT
Heavy Winds | High (4) | Likely(4) | EXTREME
Fire | High (4) | Likely(4) | EXTREME
Floods | High (4) | Possible(3) | HIGH
Sand storm | Moderate(3) | Unlikely(2) | MEDIUM

## Slide 27
RISK DESCRIPTION | RISK SEVERITY | RISK LIKELIHOOD | IMPACT
Volcano | High (4) | Very Unlikely (1) | LOW
Terrorism | Catastrophic (5) | Unlikely (2) | HIGH
Corrosion | High (4) | Possible(3) | HIGH
Lead contained in PV cells | High (4) | Very Unlikely (1) | LOW

## Slide 28
RISK DESCRIPTION | RISK SEVERITY | RISK LIKELIHOOD | IMPACT
Unacceptable environment al impacts | High(4) | Possible(3) | HIGH
Thefts | High (4) | Possible (3) | HIGH
Cyber Attacks | Catastrophic (5) | Possible (3) | EXTREME

## Slide 29
REFERENCES

## Slide 30
[1]. IEA. Getting Wind and Sun onto the Grid—A Manual for Policy Makers. 2017. Available online: https://www.iea.org/reports/getting-wind-and-solar-onto-the-grid (accessed on 9 December 2020).
[2]. Allenby, B. R., and D. Sarewitz. 2011. The techno-human condition. MIT Press, Cambridge, Massachusetts, USA.
[3]. resalliance.org, 2017. https://www.resalliance.org/about. (Accessed 23 Oct 2017)
[4]. S.L. Cutter, L. Barnes, M. Berry, C. Burton, E. Evans, E. Tate, et al.
A place-based model for understanding community resilience to natural disasters
Global Environ Chang, 18 (2008), pp. 598-606

## Slide 31
[5]. Siddarthgaurav, Nicolas Chileshe, Tony MA (2011), Project risk analysis of solar energy project delays in India, 49thAuSES Annual Conference
[6]. Rodney E, Ducq, Breysse D, Ledoux Y (2015), An integrated management approach of the project and project risk, IFAC- Paperonline-48-3(2015)535-540
[7]. A. T. Bahill., Design and Testing of an Illuminance Management System, The ITEA Journal 31(1) (2010), 63-89.
[8]. American Society for Civil Engineers (2007). The New Orleans Hurricane Protection System: What Went Wrong and Why. Reston, VA: ASCE.
[9]. Vahid M Nik, A T D Perera, Deliang Chen, Towards climate resilient urban energy systems: a review, National Science Review, 2020;, nwaa134, https://doi.org/10.1093/nsr/nwaa134